## Slide 1
Inner Product Masking Revisited
Josep Balasch
Benedikt Gierlichs
Sebastian Faust

## Slide 2
Black box
Black box vs. implementation
Measure power consumption
AES encryption
Computes: Encrypt(k,m)
Key bit 0
Key bit 1
If power consumption differs for 0 and 1
 Trace may reveal key k
Power analysis attacks devastating for security!
≠ Implementation
Notes: When we design cryptographic algorithms they are typically analyzed in the so-called black-box model. For instance, for an AES the adversary has access to the inputs and outputs but no access and knowledge about the secret key k.
As we all know in practice implementations do not behave as black boxes. The adversary can obtain side-channel leakage and by this extract the bits of the secret key. For instance, in a simple power analysis an unprotected implementation may be broken by just looking at the power trace and reading the key bit-by-bit from the trace.

## Slide 3
Important countermeasure
Masking: Protect all intermediate values of computation with randomized encoding Enc
Description of algorithm, e.g., AES
What is a good masking scheme?
K’
C’
C
K
Computes AES on encoded values
Robust encoding function
Harder to exploit leakage from protected algorithm
Leaks less about k
k
Enc(k)
Notes: What is Enc? (x+r, r)
Can we generalize? Yes, n-th order security
Hardness increases with order n and with the masking function
Power analysis attacks against implementations of cryptographic algorithms
Masking countermeasure (first order, higher order)
Different masking function and MI analysis  higher algebraic complexity (why not take a function that has constant HW?)
Results summary: New masking scheme with higher algebraic complexity, Secure against n-1 order attacks in probing model,Efficient implementation
Explain construction
Explain basic idea of proof
Explain MI analysis results, talk about choice of L1
Explain some details about the implementation, including the final comparision with earlier schemes

## Slide 4
Important countermeasure
Masking: Protect all intermediate values of computation with randomized encoding Enc
Description of algorithm, e.g., AES
What is a good masking scheme?
K’
C’
C
K
Computes AES on encoded values
Robust encoding function
Harder to exploit leakage from protected algorithm
“Encoded operations” secure in t-probing model
C
M
●
+
●
Learns t intermediate values
Notes: What is Enc? (x+r, r)
Can we generalize? Yes, n-th order security
Hardness increases with order n and with the masking function
Power analysis attacks against implementations of cryptographic algorithms
Masking countermeasure (first order, higher order)
Different masking function and MI analysis  higher algebraic complexity (why not take a function that has constant HW?)
Results summary: New masking scheme with higher algebraic complexity, Secure against n-1 order attacks in probing model,Efficient implementation
Explain construction
Explain basic idea of proof
Explain MI analysis results, talk about choice of L1
Explain some details about the implementation, including the final comparision with earlier schemes

## Slide 5
Important countermeasure
Masking: Protect all intermediate values of computation with randomized encoding Enc
Description of algorithm, e.g., AES
What is a good masking scheme?
K’
C’
C
K
Computes AES on encoded values
Robust encoding function
Harder to exploit leakage from protected algorithm
“Encoded operations” secure in t-probing model
Efficient
Notes: What is Enc? (x+r, r)
Can we generalize? Yes, n-th order security
Hardness increases with order n and with the masking function
Power analysis attacks against implementations of cryptographic algorithms
Masking countermeasure (first order, higher order)
Different masking function and MI analysis  higher algebraic complexity (why not take a function that has constant HW?)
Results summary: New masking scheme with higher algebraic complexity, Secure against n-1 order attacks in probing model,Efficient implementation
Explain construction
Explain basic idea of proof
Explain MI analysis results, talk about choice of L1
Explain some details about the implementation, including the final comparision with earlier schemes

## Slide 6
Our result in a nutshell
Design new masking scheme:
Enc function: less leakage (factor 10 better than Boolean)
Masked operations: All operations proven secure in t-probing model
Efficiency: Closer to Boolean masking (factor 3 less efficient)
 Move masking schemes with more secure encoding function closer to practice
Notes: Use different encoding function
Earlier work on different masking function
Our results
What is Enc? (x+r, r)
Can we generalize? Yes, n-th order security
Hardness increases with order n and with the masking function
Power analysis attacks against implementations of cryptographic algorithms
Masking countermeasure (first order, higher order)
Different masking function and MI analysis  higher algebraic complexity (why not take a function that has constant HW?)
Results summary: New masking scheme with higher algebraic complexity, Secure against n-1 order attacks in probing model,Efficient implementation
Explain construction
Explain basic idea of proof
Explain MI analysis results, talk about choice of L1
Explain some details about the implementation, including the final comparision with earlier schemes

## Slide 7
Rest of this talk
Masking functions
Our construction
Comparison
Notes: Use different encoding function
Earlier work on different masking function
Our results
What is Enc? (x+r, r)
Can we generalize? Yes, n-th order security
Hardness increases with order n and with the masking function
Power analysis attacks against implementations of cryptographic algorithms
Masking countermeasure (first order, higher order)
Different masking function and MI analysis  higher algebraic complexity (why not take a function that has constant HW?)
Results summary: New masking scheme with higher algebraic complexity, Secure against n-1 order attacks in probing model,Efficient implementation
Explain construction
Explain basic idea of proof
Explain MI analysis results, talk about choice of L1
Explain some details about the implementation, including the final comparision with earlier schemes

## Slide 8
Masking function Enc
Simulation in HW leakage model for small d
k1
k2
…
kd+1
k
Enc
HW(k1)
+ noise
HW(k2)
+ noise
HW(kd+1)
+ noise
Leakage =
Goal: MI( Leakage ; k ) is small (Standaert et al. 09)
Common masking function: Boolean masking
(k1,...kd+1) where ki random in {0,1}8 s.t. k = k1 +...+ kd+1
k
Enc
Practice: Simulation in HW leakage model for small d
Theory: noise + large d  recover k exp. hard in d
Notes: What is Enc? (x+r, r)
Can we generalize? Yes, n-th order security
Hardness increases with order n and with the masking function
Power analysis attacks against implementations of cryptographic algorithms
Masking countermeasure (first order, higher order)
Different masking function and MI analysis  higher algebraic complexity (why not take a function that has constant HW?)
Results summary: New masking scheme with higher algebraic complexity, Secure against n-1 order attacks in probing model,Efficient implementation
Explain construction
Explain basic idea of proof
Explain MI analysis results, talk about choice of L1
Explain some details about the implementation, including the final comparision with earlier schemes

## Slide 9
Security of masking function
Boolean masking function (d=1)
k1
k
Enc
k2
k1, k2 random s.t. k=k1+k2
HW(k1) + n
HW(k2)+ n
Leakage =
Dependency between MI( Leakage ; k ) and Noise
Masking functions that leak less? Ex.:Inner product masking
Notes: Use different encoding function
Earlier work on different masking function
Our results
What is Enc? (x+r, r)
Can we generalize? Yes, n-th order security
Hardness increases with order n and with the masking function
Power analysis attacks against implementations of cryptographic algorithms
Masking countermeasure (first order, higher order)
Different masking function and MI analysis  higher algebraic complexity (why not take a function that has constant HW?)
Results summary: New masking scheme with higher algebraic complexity, Secure against n-1 order attacks in probing model,Efficient implementation
Explain construction
Explain basic idea of proof
Explain MI analysis results, talk about choice of L1
Explain some details about the implementation, including the final comparision with earlier schemes

## Slide 10
Inner product masking
Original IP masking: [DF12, BFGV12]:
L1
Ld
…
k
EncL
R1
Rd
…
L2
1
Fixed values in GF(28)/0
Random in GF(28) s.t.: <L,R> = k
Fixed public
masks
L1
Ld
…
k
Enc
R1
Rd
…
L2
Random in GF(28)/0
Random in GF(28) s.t.: <L,R> = k
Secret masks
Our changes: New IP masking
Setup:
Encode:
Secret
masks
Decoding: Dec (L,R) = <L,R>
Notes: Use different encoding function
Earlier work on different masking function
Our results
What is Enc? (x+r, r)
Can we generalize? Yes, n-th order security
Hardness increases with order n and with the masking function
Power analysis attacks against implementations of cryptographic algorithms
Masking countermeasure (first order, higher order)
Different masking function and MI analysis  higher algebraic complexity (why not take a function that has constant HW?)
Results summary: New masking scheme with higher algebraic complexity, Secure against n-1 order attacks in probing model,Efficient implementation
Explain construction
Explain basic idea of proof
Explain MI analysis results, talk about choice of L1
Explain some details about the implementation, including the final comparision with earlier schemes

## Slide 11
Security of masking function
Our masking function New IP (d=1)
1
k
Enc
L2
<L,R> = k
HW(R1) + n
HW(R2)+ n
Leakage =
Outperforms Boolean masking by factor 10
R1
R2
1
L2
Original IP masking leaks even less  more secret masks
Notes: Use different encoding function
Earlier work on different masking function
Our results
What is Enc? (x+r, r)
Can we generalize? Yes, n-th order security
Hardness increases with order n and with the masking function
Power analysis attacks against implementations of cryptographic algorithms
Masking countermeasure (first order, higher order)
Different masking function and MI analysis  higher algebraic complexity (why not take a function that has constant HW?)
Results summary: New masking scheme with higher algebraic complexity, Secure against n-1 order attacks in probing model,Efficient implementation
Explain construction
Explain basic idea of proof
Explain MI analysis results, talk about choice of L1
Explain some details about the implementation, including the final comparision with earlier schemes

## Slide 12
Why new IP masking?
Original IP masking: Proof only for large d
(PRR14: Small first order leakage that vanishes with large d)
Next: High-level idea of construction
Main improvement
Security of masked computation
New IP: Provable secure for any d in probing model
No proof in probing model
Notes: Use different encoding function
Earlier work on different masking function
Our results
What is Enc? (x+r, r)
Can we generalize? Yes, n-th order security
Hardness increases with order n and with the masking function
Power analysis attacks against implementations of cryptographic algorithms
Masking countermeasure (first order, higher order)
Different masking function and MI analysis  higher algebraic complexity (why not take a function that has constant HW?)
Results summary: New masking scheme with higher algebraic complexity, Secure against n-1 order attacks in probing model,Efficient implementation
Explain construction
Explain basic idea of proof
Explain MI analysis results, talk about choice of L1
Explain some details about the implementation, including the final comparision with earlier schemes

## Slide 13
Our transformation
C
K
a
b
c
mult
mult
mult
output
neg
A
B
C
mult
R s.t. <L,R>=a∧b
R’ s.t. <L,R’>=b∧c
Dec
EncL
a
b
c
output
mult
R’’
mult
neg
Topology preserving
2. Operations
1. Intermediate values r
1. R = EncL(r)
2. Protected operations:
Computing on IP encodings
Fix public L

## Slide 14
New IP multiplication
A
fixed
B
L
C
Additional pre-computation for efficiency:
L
L
Ŝ
Ŝ
a
b
L
c=ab
Random encoding

## Slide 15
New IP multiplication
A
B
C
For fixed L and Ŝ:
1. Compute tensor product Ŷ of A and B:
Observation:
Ŷ
Ŷ
Ŝ
Ŝ
Problem:
Ŷ not random and too long
A
B
Ŷ
Ŷ and Ŝ encoding of desired output:<Ŷ,Ŝ> = a*b

## Slide 16
New IP multiplication
A
B
C
For fixed L and Ŝ:
1. Compute tensor product Ŷ of A and B:
2. Sample blinding matrix Ê:
Sample random matrix Ê s.t. <Ê,Ŝ> = 0

## Slide 17
New IP multiplication
A
B
C
For fixed L and Ŝ:
1. Compute tensor product Ŷ of A and B:
2. Sample blinding matrix Ê:
3. Compute Ŵ as blinded version of Ŷ:
Ŵ
Ŷ
Ê
Observation:
By linearity: <Ŵ,Ŝ> = <Ŷ+Ê,Ŝ> = ab + 0
One Problem remains: Compress Ŵ to C

## Slide 18
New IP multiplication
A
B
C
For fixed L and Ŝ:
1. Compute tensor product Ŷ of A and B:
2. Sample blinding matrix Ê:
3. Compute Ŵ as blinded version of Ŷ:
4. Compress(Ŵ, Ŝ)  C
Security: Crucial for security proof that Step 1 and Step 4 are carried out in careful way

## Slide 19
Our result
Theorem (informal): NewIP masking is secure against t-probing attacks for t < d/2
K’
C’
C
K
Efficiency: Complexity blow-up O(d2) due to multiplication
Efficient operation due to public L
Optimized affine transformation: 30% efficiency gain
Implementation of masked AES-128 on 8-bit processor
 | Boolean masking | New IP masking
d = 1 (2 secret shares) | 110k cycles | 373k cycles
d = 2 (3 secret shares) | 230k cycles | 812k cycles

## Slide 20
Comparison
Boolean
Polynomial
Original IP
New IP
Masking function Enc
Sum
Shamir
Inner prod.
Inner prod.

## Slide 21
Comparison
Boolean
Polynomial
Original IP
New IP
Robustness of Enc function
Sum
Shamir
Inner prod.
Inner prod.
Low
Good
High
Good

## Slide 22
Comparison
Boolean
Polynomial
Original IP
New IP
Security against t-probing attacks
Sum
Shamir
Inner prod.
Inner prod.
Low
Good
High
Good
t < d/2
t < d/2
No
t < d/2

## Slide 23
Comparison
Boolean
Polynomial
Original IP
New IP
Efficiency
Sum
Shamir
Inner prod.
Inner prod.
Low
Good
High
Good
t < d/2
t < d/2
No
t < d/2
Reference
“Demanding”
Factor ≈ 20
Factor ≈ 5
Main open challenge:
Get efficiency down to Boolean masking

## Slide 24
Thank you!

## Slide 25
New IP multiplication
A
fixed
B
L
C
Additional pre-computation for efficiency:
L
L
Ŝ
Ŝ
a
b
L
c=ab
Random encoding

## Slide 26
New IP multiplication
A
B
C
For fixed L and Ŝ:
1. Compute tensor product Ŷ of A and B:
Observation:
Ŷ
Ŷ
Ŝ
Ŝ
Problem:
Ŷ not random and too long
A
B
Ŷ
Ŷ and Ŝ encoding of desired output:<Ŷ,Ŝ> = a*b

## Slide 27
New IP multiplication
A
B
C
For fixed L and Ŝ:
1. Compute tensor product Ŷ of A and B:
2. Sample blinding matrix Ê:
Sample random matrix Ê s.t. <Ê,Ŝ> = 0

## Slide 28
New IP multiplication
A
B
C
For fixed L and Ŝ:
1. Compute tensor product Ŷ of A and B:
2. Sample blinding matrix Ê:
3. Compute Ŵ as blinded version of Ŷ:
Ŵ
Ŷ
Ê
Observation:
By linearity: <Ŵ,Ŝ> = <Ŷ+Ê,Ŝ> = ab + 0
One Problem remains: Compress Ŵ to C

## Slide 29
New IP multiplication
A
B
C
For fixed L and Ŝ:
1. Compute tensor product Ŷ of A and B:
2. Sample blinding matrix Ê:
3. Compute Ŵ as blinded version of Ŷ:
4. Compress(Ŵ, Ŝ)  C
Security: Crucial for security proof that Step 1 and Step 4 are carried out in opposed way
Complexity: Better complexity due to pre-computation

## Slide 30
Important countermeasure
Masking: Protect all intermediate values of computation with randomized encoding Enc
Description of algorithm, e.g., AES
What is a good masking scheme?
K’
C’
C
K
Computes AES on encoded values
Robust encoding function
Harder to exploit leakage from protected algorithm
Secure method to compute with encodings
A=Enc(a)
B=Enc(b)
Enc(c=ab)
Multiplication
Notes: What is Enc? (x+r, r)
Can we generalize? Yes, n-th order security
Hardness increases with order n and with the masking function
Power analysis attacks against implementations of cryptographic algorithms
Masking countermeasure (first order, higher order)
Different masking function and MI analysis  higher algebraic complexity (why not take a function that has constant HW?)
Results summary: New masking scheme with higher algebraic complexity, Secure against n-1 order attacks in probing model,Efficient implementation
Explain construction
Explain basic idea of proof
Explain MI analysis results, talk about choice of L1
Explain some details about the implementation, including the final comparision with earlier schemes

## Slide 31
Important countermeasure
Masking: Protect all intermediate values of computation with randomized encoding Enc
Description of algorithm, e.g., AES
k
Enc
What is a good masking scheme?
K’
C’
C
K
Computes AES on encoded values
Robust encoding function
Secure method to compute with encodings
Efficient
Harder to exploit leakage from protected algorithm
Notes: What is Enc? (x+r, r)
Can we generalize? Yes, n-th order security
Hardness increases with order n and with the masking function
Power analysis attacks against implementations of cryptographic algorithms
Masking countermeasure (first order, higher order)
Different masking function and MI analysis  higher algebraic complexity (why not take a function that has constant HW?)
Results summary: New masking scheme with higher algebraic complexity, Secure against n-1 order attacks in probing model,Efficient implementation
Explain construction
Explain basic idea of proof
Explain MI analysis results, talk about choice of L1
Explain some details about the implementation, including the final comparision with earlier schemes

## Slide 32
2. Ingredient: Operations
A=Enc(a)
Design masked operations that compute with Enc
B=Enc(b)
Enc(c=ab)
a=Dec(A)
b=Dec(B)
c=ab
C=Enc(c)
Secure masked computation: t-probing model
c is unprotected
Description of algorithm, e.g., AES
C
K
C
M
●
+
●
Computes AES on encoded values
t-probing secure: Adversary learns nothing even when he learns t intermediate values
t-probing security: to show soundness of masking
Notes: What is Enc? (x+r, r)
Can we generalize? Yes, n-th order security
Hardness increases with order n and with the masking function
Power analysis attacks against implementations of cryptographic algorithms
Masking countermeasure (first order, higher order)
Different masking function and MI analysis  higher algebraic complexity (why not take a function that has constant HW?)
Results summary: New masking scheme with higher algebraic complexity, Secure against n-1 order attacks in probing model,Efficient implementation
Explain construction
Explain basic idea of proof
Explain MI analysis results, talk about choice of L1
Explain some details about the implementation, including the final comparision with earlier schemes

## Slide 33
Masking function Enc
Simulation in HW leakage model for small d
k1
k2
…
kd+1
k
Enc
HW(k1)
+ noise
HW(k2)
+ noise
HW(kd+1)
+ noise
Leakage =
Goal: MI( Leakage ; k ) is small (Standaert et al. 09)
Common masking function: Boolean masking
(k1,...kd+1) where ki random in {0,1}8 s.t. k = k1 +...+ kd+1
k
Enc
Practical robustness of Enc?
Learns nothing about k given d shares
Notes: What is Enc? (x+r, r)
Can we generalize? Yes, n-th order security
Hardness increases with order n and with the masking function
Power analysis attacks against implementations of cryptographic algorithms
Masking countermeasure (first order, higher order)
Different masking function and MI analysis  higher algebraic complexity (why not take a function that has constant HW?)
Results summary: New masking scheme with higher algebraic complexity, Secure against n-1 order attacks in probing model,Efficient implementation
Explain construction
Explain basic idea of proof
Explain MI analysis results, talk about choice of L1
Explain some details about the implementation, including the final comparision with earlier schemes